## Slide 1: Remotely Operated Vehicle (ROV)
Iqmal Hakimi Bin Razali
1912103

## Slide 2: History of rov
The Marine Technological Society's Remotely Operated Vehicle Committee states that while it's unclear who exactly is to credit for creating the first ROV, two people are deserving of recognition. The PUV (Programmed Underwater Vehicle) was a torpedo created by Luppis-Whitehead Automotive in Austria in 1864, but Dimitri Rebikoff created the first tethered ROV in 1953 under the name POODLE.
The U.S. Navy started developing robots to help find and retrieve undersea ordnance in the late 1960s. Commercial businesses started using the technology to help the oil and gas sector in the 1980s. Nowadays, ROVs are utilized for a wide range of exploratory and business purposes, including evidence collection, pipeline maintenance, aquaculture, and drowning victim recovery, in addition to dam and water tank inspections.
ROVs can now be classified as Science-Class or Working-Class vehicles depending on whether they are employed for industrial surveillance or ocean exploration.

## Slide 3: Applications
Offshore Energy
  General Visual Inspection
  Close Visual Inspections
  NDT Inspections
  Infrastructure Deployment and Recovery
  Control Manifold Interventions
Military
  Submarine Rescue
  Waterborne Improvised Explosive Device (WIED) Intervention
  Sea and Limpet Mine Intervention
  Special Recovery
  Naval Asset Inspections
  Hydrography
Oceanography and Marine Science
  Coral and Marine Life Observation
  Sample and Sediment Collection
  Academic Research Applications
Inshore Infrastructure
  Condition Assessment and Monitoring
  Sediment Sampling
  Removal of Sludge by Dredging
  Debris Collection
Search and Rescue
  Drowned Victim Recovery
  Forensic Assessment
  Equipment Recovery
  Large Scale Search and Documentation
Commercial Diving and Salvage
  Attaching and releasing hooks for equipment installation and recovery
  Construction and salvage
Aquaculture
  Equipment and infrastructure monitoring
  Rope management and recovery
  Net Repair
  Mort Retrieval
Nuclear Decommissioning
  Fuel Rod Management
  Debris Collection and Removal
  General Visual Inspection
  Cutting and Recovery
  NDT Inspections

## Slide 4: Main Components of ROV
Hull Design
Propulsion System
Navigation System & Control
Data Collection
Data Transmission
Power Management

## Slide 5: Hull Design

## Slide 6: Propulsion System
A method of locomotion is a requirement for every mobile robotic system in order to move the robot. Because of this, thrusters are utilized to maneuver the ROV.
Each ROV system's thrusters must be carefully considered during design. If the ROV doesn't have enough thrust, the environment may overwhelm it and prevent it from carrying out the required activities.
Electrical, hydraulic, ducted jet, or a combination of the three can all be used as thrusters.

## Slide 7: Propulsion System

## Slide 8: Navigation System & Control
Camera
  A pilot's knowledge of their surroundings serves as the foundation of positional awareness. With a data tether, ROVs may transmit real-time 4K video feeds to the operator on the surface.
Inertial Measurement Unit (IMU)
  A three-axis gyroscope, a compass, and a three-axis accelerometer are all found on a sensor chip known as an IMU. They are present in all smart gadgets, including smartphones, virtual reality headsets, and robotic arms. This data will be combined by an internal algorithm to get a best estimate of direction in three dimensions.
Depth Sensor
  The ROV's depth below the surface can be determined using precisely calibrated pressure sensors. This enables autonomous depth control and navigation.
Multibeam Imaging Sonar
  This technology is essentially digital echo-location and is like magic hearing with sound. To provide you with real-time video of what is in front of the ROV without using the camera, hundreds of sound beams are shot off at once. It resembles a medical ultrasound in some ways, but it is considerably simpler to read. This can be used to locate missing items on the seafloor or for navigation by identifying underwater landmarks. Even small structures can be inspected by the high frequency multibeam with an amazing millimeter resolution.

## Slide 9: Navigation System & control
Ultra Short Baseline (USBL) aka underwater GPS
  A surface beacon receives a ping from a sonar beacon mounted on the ROV, and the position of the surface beacon is triangulated using transducers millimeters apart. The term "Ultra-Short Baseline" refers to the millimeter baselines (distances between the triangulation locations). GPS data is linked with the ROV's location in relation to the topside beacon to provide the ROV's current latitude and longitude.
Doppler Velocity Log (DVL)
  This sensor makes use of sonar transducers that are pointed in four directions towards the ocean below and function like police speed guns. Using the Doppler Effect, it determines the ROV's velocity and speed by measuring the change in frequency (pitch). It can also determine the altitude above the bottom and the reaction time of these sonar pings. This can help with autonomous depth holding and USBL data quality. The most intriguing application for this data is autonomous position hold, which paves the door for full autopilot and enables the ROV to battle currents without the need for human involvement.

## Slide 10: Navigation System & Control

## Slide 11: Data Collection
In addition to lights, sonar equipment, and a buoyancy foam pack that keeps the ROV light and manoeuvrable in the water, standard ROV components include video cameras that send real-time surveillance to scientists aboard the surface vessel.
Measurements of conductivity, temperature, and depth can be made by ROVs using external sensors mounted on the craft.
A manipulator arm is frequently included into ROVs to gather biological and geological samples, which are then placed in boxes along the edges of the ROVs.
Pilots on the surface vessel use joysticks and touchscreens on a "control box" to direct the movement of the ROV and its manipulator arms.

## Slide 12: Data Collection

## Slide 13: Data Transmission

## Slide 14: Data Transmission
It is possible to use 2.4 GHz Wifi Communication for transmitting sensor data for underwater applications on very shallow water (< 20 cm depth). This method can be used for underwater monitoring by combining the advantage of electromagnetic and acoustic communications.
Some manufacturers have modified TCP/IP, RS-485, and other industry-standard protocols for such transfers. Although beneficial and seemingly commonplace in the computer industry, the most used protocol, RS-232, is distance limited by conductors, which causes transmission issues over extended lengths of tether.

## Slide 15: Power Management